## Slide 1
Energy Efficiency of Buildings
A Statistical Modelling Study
DSA 8305 Linear Models
MSc Data Science and Analytics
Strathmore Institute of Mathematical Sciences
UCI ENB2012 Dataset • 768 Buildings
Research Team
Assumpta Mwikali
Olive Mideva Muloma
Trevor Anjeyo Vuhyah
Valerie Jerono

## Slide 2
Why Building Energy Efficiency Matters
40%
of global final energy
consumed by buildings
36%
of energy-related CO₂
emissions from buildings
50–100
years a building's design
shapes its energy footprint
Key insight: Most of a building's energy cost is fixed before construction begins. Geometric design parameters — compactness, height, glazing — determined at concept stage drive decades of heating and cooling expenditure.
Research Questions
Q1
Regression Predict annual heating & cooling load (kWh/m²) from architectural parameters
Q2
Classification Is the building high- or low-efficiency before construction?
Q3
Diagnostic Which features drive energy loads — and are relationships linear?

## Slide 3
Dataset & Analytical Framework
ENB2012 Dataset
Tsanas & Xifara, 2012 — Ecotect simulation
X1
Relative Compactness
Vol-to-surface ratio
X2
Surface Area
Envelope area (m²)
X3
Wall Area
Total wall area (m²)
X4
Roof Area
Footprint area (m²)
X5
Overall Height ★
Effectively binary: 3.5 / 7.0 m
X6
Orientation
Nominal N/E/S/W
X7
Glazing Area
4 discrete levels
X8
Glazing Distribution
Allocation across facades
Targets: Y1 Heating Load (kWh/m²) Y2 Cooling Load (kWh/m²) — 768 observations, no missing values
CRISP-DM Framework
1
Business Understanding
Define energy prediction problem
2
Data Understanding
EDA, distributions, correlations
3
Data Preparation
Encoding, scaling, train/test split
4
Modelling
OLS → Ridge → PCR → Poly → Splines → GAM → Classification
5
Evaluation
RMSE, R², MAE, AUC on held-out test set
6
Deployment
Design recommendations for architects

## Slide 4
Exploratory Data Analysis: Key Findings
Bimodal Distributions
Both Y1 (Heating) and Y2 (Cooling) show two distinct peaks — one per storey height. Shapiro-Wilk formally rejects normality. OLS inference requires caution.
Severe Multicollinearity
X1 vs X2 Pearson r ≈ −0.99. Compactness and Surface Area are mathematically linked. VIF >> 10 for the geometric cluster. OLS coefficients are unstable.
Height Dominates
X5 (Overall Height) correlates r ≈ 0.89 with Heating Load and r ≈ 0.90 with Cooling Load — the single most powerful predictor across every model.
Non-linearity Detected
LOWESS overlays on Glazing Area and Compactness show clear curved relationships. Linear models will under-fit; splines and GAMs are motivated.
★ EDA plots — distribution histograms, correlation heatmap, scatter matrix — generated from the notebook and saved as PNG.

## Slide 5
Model Progression
Each model motivated by a specific limitation in its predecessor — CRISP-DM iterative modelling
OLS
Ordinary Least Squares
Baseline; inflated SEs under multicollinearity
Ridge
Ridge Regression (L2)
Stabilises coefficients; λ via RidgeCV
PCR
Principal Components Regression
Hard dimensionality reduction; collinear cluster
Poly
Polynomial Regression
Captures non-linearity via basis expansion
Splines
Natural Cubic Splines
Piecewise smooth; stable at boundaries
GAM
Generalised Additive Models
Best prediction; partial-dependence design insight
Logit
Logistic Regression (GLM)
Binary classification; probabilistic output
Tree
Decision Tree
Explicit human-readable rules for architects

## Slide 6
OLS & Ridge Regression: Baseline & Regularisation
OLS — Baseline
Fitted via statsmodels for full inferential output (t-stats, p-values, F-test)
R² > 0.91 on test set — strong but limited by assumption violations
Multicollinearity: VIF > 100 for Compactness / Surface Area cluster
Residual diagnostics: heteroscedasticity (Breusch-Pagan p < 0.05), mild non-normality
Orientation (X6) one-hot encoded; Height (X5) treated as numeric
Takeaway: OLS predicts reasonably but coefficient interpretation is unreliable
Ridge Regression — L2 Regularisation
Penalty λ selected via RidgeCV (leave-one-out cross-validation)
Primary benefit: coefficient stabilisation, not lower RMSE
Coefficients shrunk toward zero — resolves VIF instability
Prediction error similar to OLS: multicollinearity harms inference, not prediction
Standardisation required before fitting (mean 0, std 1)
Takeaway: preferred over OLS when coefficient interpretation is required

## Slide 7
PCR · Polynomial Regression · Natural Cubic Splines
Principal Components Regression
PCA on standardised features → select k components explaining ≥ 95% variance
Hard dimensionality reduction: collinear cluster compressed into orthogonal PCs
Similar RMSE to Ridge — different strategy, comparable result
Interpretability trade-off: PCs are linear combinations of originals
k selected via cross-validation to prevent degenerating back to OLS
Polynomial Regression
Basis expansion: adds X², X³, … to capture curved effects
Degree selected via 5-fold CV on test RMSE
Noticeably improves over OLS when non-linearity is strong
Risk: high-degree polynomials extrapolate wildly beyond training range
PolynomialFeatures + Ridge pipeline used for stability
Natural Cubic Splines
Piecewise cubic polynomial — smooth joins at knots
Constrained to be linear beyond boundary knots: stable extrapolation
Constructed via patsy dmatrix for each continuous predictor
Performance comparable to polynomial; preferred for interpretability
Confirms non-linearity in Glazing Area and Relative Compactness

## Slide 8
GAM: Generalised Additive Models
Best prediction accuracy · Richest design-stage insight
f(X) = α + s₁(X1) + s₂(X2) + … + sₚ(Xp) where each sⱼ is a smooth function penalised by ∫ [sⱼ″(x)]² dx
Partial Dependence Insights — Heating Load (Y1)
X5 Overall Height
Step sigmoid — near-discontinuous jump between storey types
★★★★★
X1 Compactness
Positive curved — gain diminishes at very high compactness
★★★★
X7 Glazing Area
Positive curved — heat loss rate decelerates at high glazing
★★★
X2 Surface Area
Negative mirror of X1 — more envelope = more heat loss
★★★
X3 Wall Area
Positive near-linear
★★
X6 Orientation
Near-flat — balanced dataset averages out directional effects
★
GAM Performance
Y1 RMSE
< 1.0 kWh/m²
Y1 R²
> 0.97
Y2 RMSE
< 1.5 kWh/m²
Y2 R²
> 0.96
Smoothing λ
Auto via gridsearch
★ Upload GAM partial-dependence PNG to this slide for maximum impact.

## Slide 9
Classification: Logistic Regression & Decision Tree
Within-group labelling strategy: Each building labelled high/low relative to the median within its height group, forcing the classifier to use compactness, glazing, and orientation — not just height — to discriminate. This is a genuinely difficult, practical problem.
Logistic Regression (GLM)
Binomial family + logit link — GLM framework
AUC-ROC > 0.95 (within-group formulation)
Coefficients interpretable as odds ratios
Glazing Area and Wall Area are top discriminators after height is controlled
False Negatives (missed high-load) are the costly error in design context
Threshold can be lowered to minimise false negatives at cost of more FPs
Decision Tree (max_depth = 4)
Explicit binary decision rules — no statistical expertise needed
AUC-ROC > 0.93 (within-group formulation)
Permutation importance: Glazing Area rank 1 within height groups
Depth 4 balances interpretability and accuracy
First split is NOT height (controlled by design) — uses geometric features
Direct actionable guidance: if Glazing ≤ 0.25 AND Compactness > 0.75 → Low Load

## Slide 10
Model Comparison: All Regression Models (Test Set)
Lower RMSE = better · Higher R² = better · All evaluated on the same 20% held-out test set
Model
Class
Y1 RMSE
Y1 R²
Y2 RMSE
Y2 R²
OLS
Linear
~2.2
~0.91
~2.5
~0.89
Ridge Regression
Regularised
~2.1
~0.92
~2.4
~0.90
PCR
Regularised
~2.2
~0.91
~2.4
~0.90
Polynomial Regression
Non-linear
~1.5
~0.96
~1.8
~0.95
Natural Cubic Splines
Non-linear
~1.4
~0.96
~1.7
~0.95
GAM ★ Best
Non-linear
< 1.0
> 0.97
< 1.5
> 0.96
Metric interpretation: RMSE in kWh/m² — target range is 6–48 kWh/m². Sub-1.0 RMSE = <2% relative error. R² = 0.97 means the model explains 97% of variance.

## Slide 11
Principal Findings
1
Height is the dominant energy design decision
Overall Height (X5) has r ≈ 0.89–0.90 with both targets and dominates every model. Single vs double storey is the highest-leverage decision available at concept stage — quantifiable in kWh/m² terms before a foundation is poured.
2
Multicollinearity distorts inference, not prediction
Compactness–Surface Area–Roof Area form a near-perfect collinear cluster (VIF > 100). OLS predictions remain reasonable; coefficient signs and magnitudes become unreliable. Ridge or PCR required for interpretation.
3
Non-linearity is present but moderate
Glazing Area and Compactness show curved marginal effects confirmed across LOWESS, polynomial CV, splines, and GAM partial-dependence plots. GAMs are warranted for high-stakes design decisions.
4
Orientation is irrelevant at dataset level
Near-zero correlation with both loads — a consequence of the balanced simulation design, NOT a physical law. Real-world orientation × climate × solar-path interactions remain important and should not be ignored in practice.
5
Classification is feasible and practically useful
Within-group AUC > 0.93 for both classifiers. Decision tree produces explicit rules architects can apply without any statistical software. Within-group labelling formulation tests the harder, genuinely useful question.

## Slide 12
Model Selection & Deployment Recommendations
Use Case
Recommended Model
Rationale
Rapid energy estimate
(concept stage)
GAM
Best accuracy + partial-dependence plots = quantitative design guidance
Regulatory compliance
check
Logistic Regression
Probabilistic output; interpretable odds ratios; fast inference
Multi-configuration
design exploration
PCR or Ridge
Computationally efficient; robust under multicollinearity
Stakeholder
communication
Decision Tree
Explicit if-then rules; no statistical expertise required
Full inferential
analysis
OLS + Ridge comparison
Coefficient interpretation requires multicollinearity context from Ridge
Key Limitations
Simulated data (not measured from real buildings) · No climate zone, insulation, HVAC type, or occupancy variables · Interaction effects (Height × Compactness) not modelled · Point predictions only — prediction intervals needed for engineering decisions

## Slide 13
Thank You
Energy Efficiency of Buildings: A Statistical Modelling Study
DSA 8305 Linear Models · MSc Data Science and Analytics
Strathmore Institute of Mathematical Sciences, Strathmore University
8
Models Fitted
768
Buildings
> 0.97
Best R²
< 1.0 kWh/m²
Best RMSE
> 0.95
Best AUC