## Slide 1
ENERGY EFFICIENCY
of Buildings
A Statistical Modelling Study
Predicting Heating & Cooling Loads from Architectural Design
UCI ENB2012 Dataset
8 Models
CRISP-DM Framework
768 Buildings
Mwikali · Muloma · Vuhyah · Jerono
MSc Data Science & Analytics | Strathmore University | DSA 8305 Linear Models

## Slide 2
PROJECT
OVERVIEW
Buildings consume ~40% of global final energy. Design decisions made at concept stage lock in decades of energy cost. This study quantifies which architectural features matter most — and by how much.
Predict annual heating & cooling loads
Compare 8 modelling techniques
Uncover key design drivers
Guide energy-efficient architecture
768
Building
Configurations
8
Architectural
Parameters
40%
Global Energy
Consumed by Buildings
8
Models
Evaluated
<1.0
Best RMSE
(kWh/m²)
0.95+
Best
AUC-ROC
Building Energy Efficiency — Statistical Modelling Study

## Slide 3
THE ENB2012 DATASET
UCI Machine Learning Repository | Tsanas & Xifara (2012)
Var | Feature | Type | Range
X1 | Relative Compactness | Continuous | 0.62–0.98
X2 | Surface Area (m²) | Continuous | 514–808
X3 | Wall Area (m²) | Continuous | 245–416
X4 | Roof Area (m²) | Continuous | 110–221
X5 | Overall Height (m) | Binary | 3.5 or 7.0
X6 | Orientation | Nominal | N / E / S / W
X7 | Glazing Area | Discrete | 0, 0.10, 0.25, 0.40
X8 | Glazing Distribution | Ordinal | 0–5
TARGET VARIABLES
Y1 · Heating Load (kWh/m²)
Annual heating energy demand per unit floor area
Y2 · Cooling Load (kWh/m²)
Annual cooling energy demand per unit floor area
Key Structural Notes
▸ X5 is functionally binary (3.5m vs 7.0m)
▸ X6 is nominal — one-hot encoding required
▸ No missing values — dataset is complete
Building Energy Efficiency — Statistical Modelling Study

## Slide 4
EDA: TARGET VARIABLE DISTRIBUTIONS
Heating Load (Y1) Distribution
Chart: Heating Load (kWh/m²)
| 6–10 | 10–14 | 14–18 | 18–22 | 22–26 | 26–30 | 30–34 | 34–38 | 38–43 | 43+
Frequency | 52 | 95 | 68 | 28 | 12 | 35 | 110 | 85 | 55 | 28
⚠ Bimodal distribution — two peaks correspond to single-storey (low loads) and double-storey (high loads) buildings.
Cooling Load (Y2) Distribution
Chart: Cooling Load (kWh/m²)
| 10–14 | 14–18 | 18–22 | 22–26 | 26–30 | 30–34 | 34–38 | 38–42 | 42–46 | 46+
Frequency | 18 | 45 | 90 | 88 | 70 | 95 | 82 | 65 | 38 | 20
Shapiro-Wilk test formally rejects normality (p < 0.001). Both targets show significant positive skew — motivates flexible non-linear models.
Building Energy Efficiency — Statistical Modelling Study

## Slide 5
EDA: FEATURE CORRELATIONS & MULTICOLLINEARITY
Pearson Correlations with Target Variables
Chart: 
| X1 Compactness | X2 Surface Area | X3 Wall Area | X4 Roof Area | X5 Height | X6 Orientation | X7 Glazing | X8 Glazing Dist.
Heating Load (Y1) | 0.62 | -0.67 | 0.46 | -0.87 | 0.89 | 0 | 0.27 | 0.08
Cooling Load (Y2) | 0.64 | -0.67 | 0.42 | -0.87 | 0.9 | -0.01 | 0.21 | 0.07
X5 Height: Dominant Predictor
r ≈ 0.89 with Y1 and 0.90 with Y2. Single most important architectural decision — doubles internal volume.
Severe Multicollinearity
X1 & X2 correlate at r = −0.99. Compactness and Surface Area are mathematically linked. VIF >> 10.
X6 Orientation: Irrelevant
Near-zero correlation with both targets. Balanced dataset averages out orientation effects.
Building Energy Efficiency — Statistical Modelling Study

## Slide 6
MODELLING FRAMEWORK
CRISP-DM · Progressive Model Complexity · Each model motivated by the last
1
Business
Understanding
2
Data
Understanding
3
Data
Preparation
4
Modelling
5
Evaluation
6
Deployment
Implications
8-MODEL PROGRESSION
1
OLS Regression
Parametric Baseline
2
Ridge Regression
Regularisation (L2)
3
PCR
Dimensionality Reduction
4
Polynomial Regression
Non-linear Parametric
5
Natural Cubic Splines
Piecewise Smooth
6
GAM
Semi-parametric Flexible
7
Logistic Regression
Binary Classification
8
Decision Tree
Non-parametric Rules
Building Energy Efficiency — Statistical Modelling Study

## Slide 7
MODEL PERFORMANCE COMPARISON
Test RMSE — Heating Load (Y1)
Lower = Better · kWh/m²
Chart: 
| OLS | Ridge | PCR | Polynomial | Splines | GAM
RMSE (Y1) | 2.05 | 1.98 | 1.95 | 1.52 | 1.38 | 0.92
Test R² — Heating Load (Y1)
Higher = Better · Proportion of variance explained
Chart: 
| OLS | Ridge | PCR | Polynomial | Splines | GAM
R² (Y1) | 0.919 | 0.922 | 0.924 | 0.958 | 0.964 | 0.986
GAM
Best Model
0.92
Heating RMSE
0.986
Heating R²
0.95+
AUC-ROC
−55%
RMSE vs OLS
Building Energy Efficiency — Statistical Modelling Study

## Slide 8
KEY FINDINGS
01
Building Height is the #1 Energy Decision
Overall Height (X5) shows r ≈ 0.89 with both energy loads — single most powerful predictor. Double-storey buildings require ~2× the energy of equivalent single-storey designs. This decision is made at concept stage and can't be undone after construction.
02
Geometric Multicollinearity Distorts OLS
X1 (Compactness) and X2 (Surface Area) correlate at r = −0.99. VIF values exceed 10×. OLS coefficients are individually unreliable — Ridge & PCR restore stability. Predictions are unbiased; individual coefficient interpretation is not.
03
Non-linearity is Real but Moderate
GAM partial dependence plots confirm curved relationships for Glazing Area and Compactness. Polynomial + Spline models outperform OLS by ~25%. Non-linearity is meaningful enough to warrant flexible models in high-stakes decisions.
04
Classification is Feasible & Practical
Within-group labelling (controlling for height) creates a challenging, meaningful classification task. Logistic Regression and Decision Tree both achieve AUC > 0.95 — enabling go/no-go design decisions without full energy simulation.
Building Energy Efficiency — Statistical Modelling Study

## Slide 9
MODEL SELECTION GUIDE
Use Case | Recommended Model | Rationale
Rapid energy estimate (concept stage) | GAM | Best predictive accuracy + interpretable partial dependence plots for design guidance
Regulatory compliance check | Logistic Regression | Probabilistic output; interpretable coefficients; fast inference
Design exploration (multiple configs) | PCR or Ridge | Computationally efficient; robust under multicollinearity
Stakeholder communication | Decision Tree | Explicit rules; no statistical expertise required by architects
Full inferential analysis | OLS + Ridge | Coefficient interpretation with multicollinearity context
Limitations:
Simulated data (Ecotect) · Missing: climate zone, insulation spec, HVAC type, occupancy patterns · No interaction modelling · Point predictions only (no prediction intervals yet)
Building Energy Efficiency — Statistical Modelling Study

## Slide 10
DESIGN FOR ENERGY.
Build for the future.
The design decisions made before construction begins determine 50+ years of energy cost. This study provides a statistical lens that converts architectural geometry into quantitative energy predictions — turning intuition into evidence.
Architects gain a quantitative design tool at concept stage
GAM achieves sub-1.0 RMSE — engineering-grade precision
Applicable across East Africa's construction boom
Mwikali · Muloma · Vuhyah · Jerono
MSc Data Science & Analytics | Strathmore University
DSA 8305 Linear Models
UCI ENB2012 · 768 Buildings · 8 Models · CRISP-DM